## Slide 1: Interventional Radiology “Doses”
Walter Huda PhD
Radiology and Radiological Science

## Slide 2: Financial Disclosures Research Support (Siemens) Consultant/Contractor (Siemens) Book Royalties (LWW, MPP) President (Huda Physics in Medicine)

## Slide 3: Cell Death & Carcinogenesis

## Slide 4
Energy transferred to electrons E
Mass of air M
Air Kerma = E/M

## Slide 5: Air Kerma  Skin Dose  “Burn”
Kerma Area Product  “Cancer Risk”

## Slide 6
Why entrance skin dose
important in IR
One half dose delivered
first 3-5 cm of tissue
Skin Doses

## Slide 7
Harmful Tissue Reactions

## Slide 8
Fluoroscopy skin doses
EAK rate ~ 10 mGy/min
↑ 3 to 4 cm of tissue; ↑ 100% dose

## Slide 9
Digital Photospot
EAK ~ 3 mGy / film
 Electronic Magnification

## Slide 10
6 frames per second (5 sec)
10 runs  Skin Dose 650 mGy
35 min Fluoro  350 mGy
Typical Skin Doses
Total Skin Dose ~ 1 Gy
(1/3rd Fluoroscopy + 2/3rd DSA)

## Slide 11
Threshold Dose ~ 2,000 mGy
Probability
Dose (Gy)

## Slide 12: Erythema ~ 5 Gy
Dry Desquamation ~ 15 Gy
Moist Desquamation ~ 10 Gy

## Slide 13: Radiation burns appear ~ 10 days after radiation exposure

## Slide 14: Interventional Reference Point (IRP)
Cumulative Dose (Gy)
15 cm

## Slide 15: IR Cumulative (IRP) Doses
Dose Operator “Sees”

## Slide 16
Dose Index [DI] = Peak Skin Dose/IRP
Peak Skin Dose

## Slide 17
356 Patients
AveragePeak Skin Dose 2 Gy [Range 0.002 to 6.7 Gy]
AverageDose Index 0.5
[Range 0.05 to 1.7]
Head Neuro-Embolization

## Slide 18
26 Patients
AveragePeak Skin Dose 1.4 Gy [Range 0.07 to 5.5 Gy]
AverageDose Index 1.0
[Range 0.6 to 1.2]
Hepatic Embolization

## Slide 20
IRP (Skin Dose)
IRP (Total Skin Dose)
Skin Dose ~ IRP Dose
Conservative/Best Option

## Slide 21
MUSC
Policy Principle
IR Patients
< 2 Gy  “No Action”
> 2 Gy  “Warn Patient”
> 5 Gy  “Physics Review”
+ “Contact Patient”

## Slide 22
AKA Dose Area Product (DAP)

## Slide 23: ~ 60 per category
Total # ~ 2,000

## Slide 24: Low of 26 Gy-cm2 (Nephrostomy Obstruction)
High of 560 Gy-cm2
(Spine AVM Embolization)

## Slide 25: Average KAP ~ 340 Gy-cm2
177 head
AVM embolization
High  1,350 Gy-cm2
Low  4 Gy-cm2

## Slide 26
Mean Patient KAP ~ 200 Gy-cm2
25th %
~ 100 Gy-cm2
75th %
~ 300 Gy-cm2

## Slide 27
Exam Protocol
100 µGy-m2 = 1 Gy-cm2

## Slide 28: Kerma Area Product (Gy-cm2)
Body Region/Projection
+Patient Size

## Slide 29
ED = 0.1 mSv / Gy-cm2
Converting KAP
Effective Dose (ED)

## Slide 30
IR Effective Doses ~ 10 to 30 mSv

## Slide 31
Typical ED’s in Radiology
Body x-ray
~ 0.2 mSv
Barium Meal
~ 5 mSv
Chest CT
~ 6 mSv
Head CT
~ 2 mSv

## Slide 32
Occupational: Legal Limit 50 mSv / yr
Natural Background ~ 3 mSv / yr
Occupational: Typical
~ 5 mSv / yr

## Slide 33
Cancer Risk (in Radiology) Uncertain
Depend on Dose, Sex and Age
10 mSv (30 year old) ~ 0.1%

## Slide 34: No maximum for “diagnostic imaging”

## Slide 35: huda@musc.edu